## Slide 1: Methodology
march, 2017

## Slide 2: Designing a balanced MR&V…
We must assume a trade-off …
  Too simple versus too complex
  Too imprecise versus totally accurate
  Cheap versus expensive

## Slide 3: Energy Eficiency Projects Scope
Small Equipment
Sustitution
Equipment modernization
EE in complex systems
Massive
No MRV (estimated)
Small equipments
Cheap
Very small SME
Don´t need to take
an insurance
Semi-Massive
MRV standarized
Medium and
standarized projects
Relative Cheap
SME
Insurable
No massive
Adhoc MRV
Big projects
Expensive
SME
Not insurable
ESI

## Slide 4: The basis: ISO50006
The new ISO standard oriented to energy baselines and performance indicators
Define energy consumption and use, and the various meanings of energy efficiency
Introduces Energy Performance Indicators (EnPIs) and Energy Baselines
Give context of quantifying energy performance

## Slide 5: The objective : Quantify energy using indicators
Método
USE
CONSUME
PERIMETER
EnPI

## Slide 6: Using standard EE Methodology …

## Slide 7: How? Measuring and comparing base line versus new operation
Fuente : Manuales ISO50006

## Slide 8: The methodology manuals and tools
To support the project structuring and contract clauses, there are different instruments :
  Manual that describes this methodology and how structure a project to be validated
  Formats that allow structure a project
  Guide to how calculate energy efficiency for each technology

## Slide 9: Calculate Energy Savings and Non-compliance is easy …
Base line EnPI: 0.80 kWh per delivered HP
Proposed EnPI : 0.40 kWh per delivered HP
Measured EnPI : 0.50 kWh per delivered HP
Commit to use : 14,000 delivered HP
Cost of energy : $1.8 per kWh used
The estimated energy saving in the period (6 months)
is 5,600 kWh -> $10,080 MXP.
Non-compliance:
(0.40 – 0.50) X (14,000 HP delivered) X $1.8
The provider must pay $2,520 to the consumer

## Slide 10: Considerations
Fuente : Manuales ISO50006
The Methodology sets a fixed price to energy consumed
The consumer agrees to use the equipment in a defined minimun level
The measurement during the base line assesment and verificartion periods is performed using controlled variables and parameters
The contract does not reward a performance beyond savings commitment

## Slide 11
THANK YOU !
Ing. Adalberto Padilla Limón
apadilla.energia@gmail.com